## Slide 1
Welcomes everyone to

## Slide 2: button
#define LED 2
#define pinButton 8
void setup() {
pinMode(pinButton, INPUT); //set the button pin as INPUT
pinMode(LED, OUTPUT); //set the LED pin as OUTPUT
Serial.begin(9600);
}
void loop() {
int stateButton = digitalRead(pinButton);
//read the state of the button
if(stateButton == 1) { //if is pressed
digitalWrite(LED, HIGH); //write 1 or HIGH to led pin
Serial.println(stateButton);
} else { //if not pressed
digitalWrite(LED, LOW); //write 0 or low to led pin
Serial.println(stateButton);
}
}

## Slide 3: SERIAL MONITOR
Used for sending and receiving data or commands .
Used for debugging.
Uses serial communication.

## Slide 4: DAC –Digital to Analog & PWM
A DAC is a circuit that allows you to translate numeric values into analog signals.
PWM & Duty Cycle
The duty-cycle is the ratio of the ON time and the total period of the wave. The ON time is the amount of time in which the wave stays at 5V and the total period is the sum of the time while it stays at 5V and 0V time.
When you use the AnalogWrite function you set the output duty cycle that may vary between 0% and 100% and you choose these values with the second parameter you pass to the function ( 0÷255).
DC = ON TIME/(OFF TIME + ON TIME)
Mean Value and Duty Cycle
The mean value of a wave is the average of the voltage provided from the output over a period time of the wave.
The square waveform with amplitude 0V-5V has a mean value that is equal to the max amplitude (5V) multiplied for the duty-cycle. This means that you can change the mean value of the PWM output by using the (AnalogWrite(pin,127)) .
You will have 2.5v Average value if you set it 50%.

## Slide 6
int led_pin = 6;
void setup() {
pinMode(led_pin, OUTPUT); //Declaring LED pin as output
}
void loop() {
for(int i=0; i<255; i++) //Fading the LED
{
analogWrite(led_pin, i);
delay(5);
}
for(int i=255; i>0; i--){
analogWrite(led_pin, i);
delay(5);
}
}

## Slide 7: Types of communication
1
SPI – Serial Peripheral Interface
2
I2c – Inter Integrated Circuit
3
UART & USART – Universal Synchronous Asynchronous Receiver Transmitter

## Slide 8: Serial Communication UART
Baud Rate
The baud rate specifies how fast data is sent over a serial line. It’s usually expressed in units of bits-per-second (bps). One of the more common baud rates, especially for simple stuff where speed isn’t critical, is 9600 bps. Other “standard” baud are 1200, 2400, 4800, 19200, 38400, 57600, and 115200.
Framing the data
Each block (usually a byte) of data transmitted is actually sent in a packet or frame of bits. Frames are created by appending synchronization and parity bits to our data.
A serial bus consists of just two wires - one for sending data and another for receiving. As such, serial devices should have two serial pins: the receiver, RX, and the transmitter, TX.

## Slide 9: I2C – Inter-integrated Circuit
The Inter-integrated Circuit (I2C) Protocol is a protocol intended to allow multiple “slave” digital integrated circuits (“chips”) to communicate with one or more “master” chips. Like the Serial Peripheral Interface (SPI), it is only intended for short distance communications within a single device. Like Asynchronous Serial Interfaces (such as RS-232 or UARTs), it only requires two signal wires to exchange information.
I2C requires a mere two wires, like asynchronous serial, but those two wires can support up to 1008 slave devices. Also, unlike SPI, I2C can support a multi-master system, allowing more than one master to communicate with all devices on the bus.
Data rates fall between asynchronous serial and SPI; most I2C devices can communicate at 100kHz or 400kHz.

## Slide 10: SPI – Serial Peripheral Interface
Serial Peripheral Interface (SPI) is an interface bus commonly used to send data between microcontrollers and small peripherals such as shift registers, sensors, and SD cards. It uses separate clock and data lines, along with a select line to choose the device you wish to talk to.
In SPI, only one side generates the clock signal (usually called CLK or SCK for Serial Clock). The side that generates the clock is called the “master”, and the other side is called the “slave”. There is always only one master (which is almost always your microcontroller), but there can be multiple slaves (more on this in a bit).
When data is sent from the master to a slave, it’s sent on a data line called MOSI, for “Master Out / Slave In”. If the slave needs to send a response back to the master, the master will continue to generate a prearranged number of clock cycles, and the slave will put the data onto a third data line called MISO, for “Master In / Slave Out”.
SPI is “full duplex”

## Slide 11: What's a Servo motor
Servo motors are DC motors that allows for precise control of angular position. They are actually DC motors whose speed is slowly lowered by the gears.
The servo motor is actually an assembly of four things: a normal DC motor, a gear reduction unit and a control circuit.

## Slide 12: How does it work ?
From the picture we can understand that the PWM signal produced should have a frequency of 50Hz that is the PWM period should be 20ms. Out of which the On-Time can vary from 1ms to 2ms.
So when the on-time is 1ms the motor will be in 0° and when 1.5ms the motor will be 90°, similarly when it is 2ms it will be 180°. So, by varying the on-time from 1ms to 2ms the motor can be controlled from 0° to 180°

## Slide 13: BASIC SWEEP program
#include <Servo.h>
Servo myservo; // create servo object to control a servo
// twelve servo objects can be created on most boards
int pos = 0; // variable to store the servo position
void setup() {
myservo.attach(9); // attaches the servo on pin 9 to the servo object
}
void loop() {
for (pos = 0; pos <= 180; pos += 1) { // goes from 0 degrees to 180 degrees
// in steps of 1 degree
myservo.write(pos); // tell servo to go to position in variable 'pos'
delay(15); // waits 15ms for the servo to reach the position
}
for (pos = 180; pos >= 0; pos -= 1) { // goes from 180 degrees to 0 degrees
myservo.write(pos); // tell servo to go to position in variable 'pos'
delay(15); // waits 15ms for the servo to reach the position
}
}

## Slide 14: Whats a ultrasonic sensor
An Ultrasonic sensor is a device that can measure the distance to an object by using sound waves. It measures distance by sending out a sound wave at a specific frequency and listening for that sound wave to bounce back. By recording the elapsed time between the sound wave being generated and the sound wave bouncing back, it is possible to calculate the distance

## Slide 15: HOW does an ultrasonic sensor work !
The module has two eyes like projects in the front which forms the Ultrasonic transmitter and Receiver.
Work on simple formulae: DISTANCE= SPEED * TIME
To calculate the distance we must now the speed and time. Speed of and ultrasonic wave in air is 344 m/s. And to measure time there is a clock and microcontroller in the circuit.
Working Voltage DC 5 V
Working Current 15mA
Working Frequency 40Hz
Max Range 4m
Min Range 2cm
MeasuringAngle 15 degree
Dimension 45*20*15mm

## Slide 16: HOW to measure distance using an ultrasonic sensor
// defines pins numbers
const int trigPin = 9;
const int echoPin = 10;
// defines variables
long duration;
int distance;
void setup() {
pinMode(trigPin, OUTPUT); // Sets the trigPin as an Output
pinMode(echoPin, INPUT); // Sets the echoPin as an Input
Serial.begin(9600); // Starts the serial communication
}
void loop()
{
digitalWrite(trigPin, LOW);
delayMicroseconds(2);
// Sets the trigPin on HIGH state for 10 micro seconds
digitalWrite(trigPin, HIGH);
delayMicroseconds(10);
digitalWrite(trigPin, LOW);
// Reads the echoPin, returns the sound wave travel time in microseconds
duration = pulseIn(echoPin, HIGH);
// Calculating the distance
distance= duration*0.034/2;
// Prints the distance on the Serial Monitor
Serial.print("Distance: ");
Serial.println(distance);
}

## Slide 17: What’s an LDR ?
An LDR(Light detecting Resistor) or a cadmium sulfide (CdS) cell is a component that has a (variable) resistance that changes with the light intensity that falls upon it. This allows them to be used in light sensing circuits.
The most common type of LDR has a resistance that falls with an increase in the light intensity falling upon the device (as shown in the image above). The resistance of an LDR may typically have the following resistances: DAY=5000ohm and DARK= 20000000ohm

## Slide 18: How does it work !
It basically works on the principle of photoconductivity.
Photoconductivity is an optical and electrical phenomenon in which a material becomes more electrically conductive due to the absorption of electromagnetic radiation.
When light falls on it the no. of electrons increases thus increasing the conductivity which implies it will have less resistance.
When it is dark the no. of electrons decreases thus decreasing the conductivity which implies it will have more resistance.

## Slide 19: Basic circuit to implement LDR
Touch switch using and LDR.

## Slide 20
#define LDRpin A0 // pin where we connected the LDR and the resistor
int LDRValue = 0; // result of reading the analog pin
void setup()
{
Serial.begin(9600); // sets serial port for communication
pinMode(13,OUTPUT);
}
void loop()
{
LDRValue = analogRead(LDRpin); // read the value from the LDR
Serial.println(LDRValue); // print the value to the serial port
if(LDRValue>=1000)
{
digitalWrite(13,HIGH);
delay(100);
}
else
{
digitalWrite(13,LOW);
delay(100);
}
delay(100); // wait a little
}